iBoardbot project
Communication protocol definition
Versión: 0.4
jjrobots.

Commands and Blocks of data description

We choose a small block data size because Arduino has a very limited RAM resources (2.5k on our ATMega32U4) and we need to store the whole block in memory for processing the commands.

Block data size (packet): 768 bytes (256*3)
Comand size: 3 bytes. One block = 256 commands.
Each command has 2 fields of 12 bits: 2x12 = 24bits = 3 bytes.
C1 = 12 bits MSB, C2 = 12 bits LSB

        111110100001 111110100001 = C1 C2 = total: 3 bytes (12+12 = 24 bits)
        ------------------- -------------------
        C1 C2

Command types:
- Coordinates (absolute coordinates in mm/10 units)
- Special (Pen lift, Eraser, Wait…)

Special commands:
LOGIC: C1 > 4000

C1 = 4009, C2 = 4001 : Block start. Message start sync bytes. HEX: FA9FA1
C1 = 4009, C2 < 4000 : Block number C2
C1 = 4001, C2 = 4001 : Start drawing. HEX: FA1FA1
C1 = 4002, C2 = xxxx : Stop drawing. HEX: FA2000
C1 = 4003, C2 = xxxx : Pen lift
C1 = 4004, C2 = xxxx : Pen down (draw)
C1 = 4005, C2 = xxxx : Enable Eraser
C2 = 4006, C2 = seg : Wait C2 seconds (max 30 seconds).
...

Coordinate commands:
LOGIC: C1 < 4000 AND C2 < 4000

C1 = X, C2 = Y. Absolute coordinates. Resolution 0.1mm
With this resolution we have a maximum 40cm x 40cm canvas size.
Standard iBoardbot canvas size is 36x12cm
DIY: For other canvas sizes, you should rescale this values on the iBoardbot firmware.

Workflow

iBoardbot poll the server with an internal iBoardbot ID and a STATUS parameters
STATUS=ready => iBoardbot is ready to receive new blocks of data (packets)
STATUS=ACK&NUM=xxx => ACK of block number xxx and ready for new blocks

Block example (draw a line):
  C1 C2 [ Hexacimal]
4009 4001 [FA9FA1] # Nuevo dibujo
4009 0001 [FA9001] # Block number (this number is calculated by the server)
4001 4001 [FA1FA1] # Start drawing (new draw)
4003 0000 [FA3000] # pen lift
0000 0000 [000000] # Move to X = 0, Y = 0
1000 1000 [3E83E8] # Move to X = 100mm, Y = 100mm
4004 0000 [FA4000] # pen down (draw)
1500 1000 [5DC3E8] # Move to X = 150mm, Y = 100mm
4003 0000 [FA3000] # Pen lift
0000 0000 [000000] # Move to 0,0
4002 0000 [FA2000] # Stop drawing (Finish).