iBoardbot API v1.0 specification

This is the documentation of the first version of the iBoardbot API. In order to use the API you need to have an APPID identifier for your iBoardbot. You can get your APPID from the APP settings page (access via the small gear wheel on the bottom of the page). Generate as many different APPIDs for your iBoardbot as you want for different applications. It's recommended to generate a new APPID specific for your API. Do this on the Admin page (at the bottom of the page populate the name field for your new APPID and press the green button).

API Functions

TEXT:

Description: This function will let you write a text on the iboardbot. You can use it in automatic mode (so the server dynamically adapts the text size and number of lines) or manually (you define the text size and position)
URL: http://ibbapp.jjrobots.com/api/v1/text.php
PARAMETERS: APPID, TEXT
OPTIONAL PARAMETERS: X (mm) ,Y(mm), SIZE (range from 1 to 5)
METHOD: GET or POST

Note: If you use GET PARAMETERS, TEXT should be “urlencoded” to avoid forbidden characters. Max recommended number of characters: 200.

Examples:
Automatic text position and size:
http://ibbapp.jjrobots.com/api/v1/text.php?APPID=XXXXXXXXXXXX&TEXT=hello%20world
Manual text position (upper,right position, small text):
http://ibbapp.jjrobots.com/api/v1/text.php?APPID=XXXXXXXXXXXX&TEXT=Great!&X=300&Y=90&SIZE=2

Note: You need to replace the XXXXXXX APPID on the examples with a valid APPID identifier of your iBoardbot. Feel free to test these examples directly on your internet browser.

CLEAR:

Description: This function let you clear the iboardbot. You could control the part of the board to wipe or clear all the board (without optional parameters)

URL: http://ibbapp.jjrobots.com/api/v1/clear.php
PARAMETERS: APPID
OPTIONAL PARAMETERS: X1 (mm) ,Y1(mm), X2(mm), Y2(mm)
   X1,Y1 are bottom,left position X2,Y2 is top right position
METHOD: GET or POST

Examples:
Clear all board:
http://ibbapp.jjrobots.com/api/v1/clear.php?APPID=XXXXXXXXXXXX
Manual clear part of the board:
http://ibbapp.jjrobots.com/api/v1/clear.php?APPID=XXXXXXXXXXXX&X1=290&Y1=85&X2=380&Y2=120

MESSAGE:

Description: This function let you write a text on the iboardbot. This function automatically clear all the board before sending the message (and after the message is written, there is a pause of 8 seconds before processing any new task(in order to let time to read the message)
You can use it in automatic mode (so the server dynamically adapts the text size and number of lines) or manually (you define the text size and position)
URL: http://ibbapp.jjrobots.com/api/v1/message.php
PARAMETERS: APPID, TEXT
OPTIONAL PARAMETERS: X (mm) ,Y(mm), SIZE (range from 1 to 5)
OPTIONAL PARAMETERS FOR CLEAR: X1 (mm) ,Y1(mm), X2(mm), Y2(mm)
METHOD: GET or POST

Note: If you use GET PARAMETERS, TEXT should be “urlencoded” to avoid forbidden characters.
This function is intended to be used with services like IFTTT so with only one call to the API you ensure is enough to wipe the board, write the message and wait some time.

Examples:
Automatic text position and size: Clear board ->Write Text->Wait
http://ibbapp.jjrobots.com/api/v1/message.php?APPID=XXXXXXXXXXXX&TEXT=hello%20world
Manual text position (upper,right position, small text):
http://ibbapp.jjrobots.com/api/v1/message.php?APPID=XXXXXXXXXXXX&TEXT=iBoardbot&X=260&Y=90&SIZE=2&X1=250&Y1=85&X2=380&Y2=110